Anexa la invitaţia de participare nr. 01-11/224 din 28.12.2009

Lista echipamentului de calcul, cantitatea şi specificaţiile tehnice

| Nr. d/r | Denumirea şi specificaţiile tehnice | Cantitatea | Garanţia (ani) |
| --- | --- | --- | --- |
| 1. | Brand Name Server | 1 | 3 |
|  | Form Factor | Tower, convertible to rack mount option |  |  |
|  | Chipset | Intel 3420 chipset |  |  |
|  | Processor | One Intel Xeon at Xeon 4C X3430 2.4GHz with 1333MHz FSB and 8MB L3 / 4 Core / with Intel Turbo Boost Technology |  |  |
|  | Memory | 4GB PC3-10600 1333MHz ECC DDR3-SDRAM |  |  |
|  | HDD | 2 x 250GB SATA |  |  |
|  | SAS/SATA controller | RAID 0,1, 1E |  |  |
|  | Graphics controller | on system board / 128MB DDR2-250MHz SDRAM |  |  |
|  | Ethernet | Dual Gigabit Ethernet ports |  |  |
|  | Power supply | 401W auto switch / Automatic Server Restart (ASR) / cooling fan in power supply (variable speed) |  |  |
|  | Diagnostics | Diagnostic LEDs / error LEDs for fans and memory / pre boot DSA integrated on system board |  |  |
|  | Systems Management | Integrated Management Module (IMM) / VSC452 / H8S2461 / TPM 1.2 / IPMI 2.0 / SOL /provides system and environmental |  |  |
| 2. | Windows Server 2003 Standard Edition R2 | 1 |  |

Conducătorul grupului de lucru:

__________________________